## Slide 1: CSE 591 Introduction to Scientific Visualization
Ross Maciejewski
rmacieje@asu.edu

## Slide 2: The Importance of Knowing Your Data
Everything you do to create an image relies on characteristics of your data !!
You should know the following:
  Data source
  Data characteristics
  Representation
  Transformations
  Quality
Slides borrowed from Dr. David S. Ebert

## Slide 3: Data Sources
The capability of traditional presentation techniques is not sufficient for the increasing amount of data to be interpreted
  Data might come from any source with almost arbitrary size
  Techniques to efficiently visualize large-scale data sets and new data types need to be developed
Slides borrowed from Dr. David S. Ebert

## Slide 4: Data Sources
Real world
  Measurements and observation
Theoretical world
  Mathematical and technical models
  Computational models
Artificial world
  Data that is designed
Slides borrowed from Dr. David S. Ebert

## Slide 5: Data Sources
Measurement
  Medical imaging (MRI, CT, PET)
  Geology (e.g. oil exploration)
  Meteorology and environment (satellites)
  Astronomy (e.g. Hubble Space Telescope 100MB/day)
  Atomic Force Microscopes, Electron Microscopes
Slides borrowed from Dr. David S. Ebert

## Slide 6: Data Sources
Computer simulations
  Computational fluid mechanics (CFD)
  Structural mechanics
    Car body design
  Chemistry and biology (molecular modeling)
  Physics (Astrophysics, computational physics)
  Computational nanoelectronics
Slides borrowed from Dr. David S. Ebert

## Slide 7: Data characteristics
Spatial data
  Scalar
  Vector
  Volumetrically varying
  Time varying
Non-spatial data
  Probability distributions
  Uncertainty information
  Accuracy, error
  Statistical information
Slides borrowed from Dr. David S. Ebert

## Slide 8: Data Characteristics
Continuity
Structure
Dimensions
Values per sample point
Type
Scale
Slides borrowed from Dr. David S. Ebert

## Slide 9: Characterization of Visualization Problems
Characterized by type of data and dimensionality
  Medical easiest
  Scientific
  Information hardest
Slides borrowed from Dr. David S. Ebert

## Slide 10: Visualization Problems vs. Data Types
Medical
Scientific
Information
2D
3D
Vector
Structured
Unstructured
Scalar
n D
2D
3D
Vector
Structured
Scalar
Tensor
Tensor
Slides borrowed from Dr. David S. Ebert

## Slide 11: Data Types and Characteristics
Structure
  Structured
    Voxel
    Rectilinear
    Curvilinear
Slides borrowed from Dr. David S. Ebert

## Slide 12: Data Types and Characteristics
Structure
  Unstructured
    Tetrahedral
Slides borrowed from Dr. David S. Ebert

## Slide 13: Data Types and Characteristics
Dimensionality
  2D
    Surfaces vs. points. vs. lines
  3D
    Scalar vs. vector
  n D
    n D space vs. multiple 3D values (e.g., CT, MR)
Slides borrowed from Dr. David S. Ebert

## Slide 14: Data Types and Characteristics
Scalar vs. vector
  Scalar easier to represent
  Vectors require more information to be displayed
    Directionality
Slides borrowed from Dr. David S. Ebert

## Slide 15: Characterization of Visualization Techniques
2D Data:
  Line plots
  Scatter plots
  Charts
Slides borrowed from Dr. David S. Ebert

## Slide 16: Characterization of Visualization Techniques
3D Data:
  Streamlines
  Particle traces
  Isosurfaces
  Glyph rendering
  Volume rendering
Slides borrowed from Dr. David S. Ebert

## Slide 17: Characterization of Visualization Techniques
3D data: streamlines
  Lines that trace out flow
  Mainly used for flow visualization
Slides borrowed from Dr. David S. Ebert

## Slide 18: Characterization of Visualization Techniques
3D data: streamlines
Slides borrowed from Dr. David S. Ebert

## Slide 19: Streamlines
Slides borrowed from Dr. David S. Ebert

## Slide 20: Ribbons
Slides borrowed from Dr. David S. Ebert

## Slide 21: Rubber Tubes
Slides borrowed from Dr. David S. Ebert

## Slide 22: LIC Flow (Banks and Interrante)
Slides borrowed from Dr. David S. Ebert

## Slide 23: LIC
Slides borrowed from Dr. David S. Ebert

## Slide 24: LIC and Dye Advection
Slides borrowed from Dr. David S. Ebert

## Slide 25: Vector Fields Direct Manipulation Widgets/Haptics
Slides borrowed from Dr. David S. Ebert

## Slide 26: Multiple Fields - Haptics
Slides borrowed from Dr. David S. Ebert

## Slide 27: Tensor Fields
Slides borrowed from Dr. David S. Ebert

## Slide 28: Hyperstreamlines
Slides borrowed from Dr. David S. Ebert

## Slide 29: Hypersurfaces
Slides borrowed from Dr. David S. Ebert

## Slide 30: Colormap e1 (Pierpaoli ’97, Jones ’97)
Principal eigenvector, anisotropy
determine color
R=abs(x)
G=abs(y)
B=abs(z)
Slides borrowed from Dr. David S. Ebert

## Slide 31: Brush Strokes (Laidlaw ’98)

## Slide 32: Characterization of Visualization Techniques
3D data: particle traces
  Particles trace out flow field
  Mainly used for flow visualization
Slides borrowed from Dr. David S. Ebert

## Slide 33: Characterization of Visualization Techniques
3D data: isosurfaces
  Create surface from constant ranges in data
  Has occlusion problems
Slides borrowed from Dr. David S. Ebert
Notes: Iso-surface: The thresholds become the solid surface

## Slide 34: 3D Scalar Field Visualization
Iso-contour surfaces
or
Iso-surfaces
Slides borrowed from Dr. David S. Ebert

## Slide 35: 3D Visualization
Can add information about an additional variable
Here, two additional variables control the color.
Slides borrowed from Dr. David S. Ebert

## Slide 36: 3D Scalar Field Visualization
Slides borrowed from Dr. David S. Ebert

## Slide 37: 3D Visualization
Can add information about an additional variable
Here, two additional variables control the color.
Slides borrowed from Dr. David S. Ebert

## Slide 38: Derived Fields
Slides borrowed from Dr. David S. Ebert

## Slide 39: Characterization of Visualization Techniques
3D data: glyph rendering
  Encodes multi-dimensional information
  Advantages of volume rendering
Slides borrowed from Dr. David S. Ebert

## Slide 40: Characterization of Visualization Techniques
3D data: volume rendering
  Visualization of entire data volume
  Map data values to opacity of volume elements
  Techniques:
    Volume tracing
    Shear-warp factorization
    Splatting
    Hardware texturing
Slides borrowed from Dr. David S. Ebert

## Slide 41: Characterization of Visualization Techniques
3D data: volume rendering
Slides borrowed from Dr. David S. Ebert

## Slide 42: Surface vs. Volume Rendering
Surface rendering
  Displays a subset of the data as surfaces
  Multiple isosurfaces may be difficult to understand
  Occlusion problems
  Interactive rendering rate even on low-cost PCs
Volume rendering
  Displays all of the data values selected
  Truer representation of volumetric data
  Transfer functions may be difficult to design
  Difficult to get interactive rendering rates
Slides borrowed from Dr. David S. Ebert

## Slide 43: Common Issues for All Types of Visualization Techniques
Accuracy of results
Accurate sampling
Hidden surface removal / rendering
Shading and illumination
Perception of information
User interaction
Slides borrowed from Dr. David S. Ebert

## Slide 44: Sampling and Visualization
Sampling performed multiple times
  Data acquisition
  Segmentation / data pre-processing
  Surface generation
  Visualization / rendering
This information is vital to generating accurate images
Slides borrowed from Dr. David S. Ebert

## Slide 45: Hidden Surface Removal (HSR) vs. Rendering
Rendering: taking a geometric description of objects / data and creating an image
HSR: determining which surface(s) is visible at each pixel in the image
Slides borrowed from Dr. David S. Ebert

## Slide 46: Shading and Illumination
Shading: determining the color of each pixel
  Includes: illumination, transparency, texturing, and shadowing
Illumination: simulating light reflectance, absorption, and transmission
Slides borrowed from Dr. David S. Ebert

## Slide 47: Shading Example:
Slides borrowed from Dr. David S. Ebert

## Slide 48: Perception’s Role in Visualization
Generating images for humans to view
Visual cues can increase effectiveness
Correct use of
  Color
  Lighting / shading
  Shape / texture
  Motion
Slides borrowed from Dr. David S. Ebert

## Slide 49: Interactive vs. Non-Interactive
Interaction vs. image quality
Interaction vs. information quantity
  More is not necessarily better
Best choice:
  System that allows interactive preview and exploration combined with non-interactive realistic rendering
Slides borrowed from Dr. David S. Ebert

## Slide 50: VR Approaches
Immersive
  Isolates the user from environment
  Expensive
  Examples: Virtual Wind Tunnel, UNC, NRL, etc.
Slides borrowed from Dr. David S. Ebert

## Slide 51: VR Approaches (cont.)
Minimally-immersive
  Access to environment
  Collaboration possible
  Low cost
  Two hands give proprioception
  Examples: Hinckley et.al, Virtual Workbench, Responsive Workbench
Slides borrowed from Dr. David S. Ebert

## Slide 52: Some Common Visualization Packages
IRIS Explorer (NAG)
  Dataflow architecture
  Supports
    Isosurfaces
    Streamlines
    Volume rendering
  Commercialized by NAG
Slides borrowed from Dr. David S. Ebert

## Slide 53: Common Visualization Packages
AVS
  One of the oldest packages & most popular
  Supports
    Isosurfaces
    Streamlines
    Volume rendering
Slides borrowed from Dr. David S. Ebert

## Slide 54: Common Visualization Packages
IBM Data Explorer (Open DX)
  Dataflow architecture
  Supports
    Isosurfaces
    Streamlines
    Volume rendering
Slides borrowed from Dr. David S. Ebert

## Slide 55: Common Visualization Packages
IBM
DX
Slides borrowed from Dr. David S. Ebert

## Slide 56: VTK (The Visualization Toolkit)
Programming interface using Tcl/TK, C++ or Java
Supports many rendering techniques
Can extend capabilities
Slides borrowed from Dr. David S. Ebert

## Slide 57: Common Visualization Packages
Ensight / CEI
  End user package
  Supports
    Isosurfaces
    Streamlines
    Volume rendering
    VR capabilities
Slides borrowed from Dr. David S. Ebert

## Slide 58: Common Visualization Packages
Dataflow
  Modeling
  Simulation
  Visualization
Slides borrowed from Dr. David S. Ebert

## Slide 59: Example Research System: Our Glyph-based Visualization System- SFA
Glyph rendering
  Data dimensions mapped to glyph attributes
Minimally-immersive VR interface
Multivariate, multidimensional time-varying data
Utilizes many perceptual cues
Slides borrowed from Dr. David S. Ebert

## Slide 60: Minimally-Immersive User Interface - Fishtank VR
Advantages
  Access to environment
  Collaboration possible
  Low cost (< $10K)
Implementation techniques
  Stereo viewing
  Two-handed interaction:
    3-space trackers with buttons
  Each hand has a distinct role
    Left hand sets up context
    Right hand performs fine manipulation
Slides borrowed from Dr. David S. Ebert

## Slide 61: Interactive Lens Visualization Techniques (Ebert and Shaw)
Three types:
  Contour plate
  Texture-based volume rendering
  X-ray projection (thin slab)
Allows display of more data variables/ dimensions
Solar Wind MHD Simulation Data
Slides borrowed from Dr. David S. Ebert

## Slide 62: Related fields
Photorealistic rendering
  The synthesis of an image of a scene as it would look like in reality
Slides borrowed from Dr. David S. Ebert

## Slide 63: Related fields
Geometric modeling
  The effective representation and efficient modification of geometric shape on a computer
Slides borrowed from Dr. David S. Ebert

## Slide 64: Related fields
Image processing and computer vision
  The manipulation of images and the extraction of object specific information from images
Slides borrowed from Dr. David S. Ebert

## Slide 65: Potential for visualization
Effectively convey multifield three-dimensional, time-varying information
Interactive exploration and analysis
Closed loop exploration
  Simulation -> visualization/exploration -> simulation
Simultaneous comparison of 4 to 7 variables
  Spatial and abstract data
  Error and uncertainty data
Slides borrowed from Dr. David S. Ebert
Notes: Analyze first
Zoom in filter
Data extraction
Analyze again

## Slide 66: Capabilities for Visualization
Advanced 3D visualization
  Interactive volume rendering
  Illustrative rendering enhancements
  Isosurfaces
  Particle clouds
  Glyphs
Slides borrowed from Dr. David S. Ebert

## Slide 67: Capabilities for Visualization
  Animation
  Stereo visualization
  3D interaction and tracking
  Haptics
  Real-time interaction and exploration
  Visual interface for computational steering
Slides borrowed from Dr. David S. Ebert

## Slide 68: Advanced Real-time Volume Visualization Examples
Images from Kniss, Premoze, Hansen, Ebert, “Interactive Translucent Volume Rendering and Procedural Modeling,” IEEE Visualization 2002.

## Slide 69: Interactive Visually Accurate Weather Visualization

## Slide 70: Example: Interactive Volume Illustration
Images by Nik Svakhine
Slides borrowed from Dr. David S. Ebert

## Slide 71: Iron Protein Molecule Normal Volume Rendering Tone Shaded .

## Slide 72: Stipple Examples

## Slide 73: Interactive Volume Illustration and Volume Stippling Results
Images by Nik Svakhine
Slides borrowed from Dr. David S. Ebert

## Slide 74: Example: Volume Rendering vs. Isosurfaces
X38 re-entry vehicle flow simulation

## Slide 75: Example: Minimally-immersive Visualization (Ebert and Shaw)
Glyph rendering
  Data dimensions mapped to glyph attributes
Minimally-immersive VR interface
Multivariate, multidimensional time-varying data
Utilizes many perceptual cues
Combines multiple rendering modalities
Applications:
  Scientific visualization (physics, CFD, comp. nanotechnology)
  Information visualization (corpus vis, network intrusion detection)
Solar Wind MHD Simulation Data
Slides borrowed from Dr. David S. Ebert

## Slide 76: CSE 591 Volume Visualization I
Ross Maciejewski
rmacieje@asu.edu

## Slide 84
Notes: Goal to look at 3D surfaces

## Slide 90
Notes: In 2D we call it contour
In 3D we call it isosurface.

## Slide 118: Readings and Homework
Required Reading:
  Lorensen, W., and Cline, H. "Marching Cubes: A high Resolution 3D Surface Reconstruction Algorithm", ACM Computer Graphics, Volume 21, Number 4, 1987.
  Penny Rheingans and David Ebert (2001), "Volume Illustration: Non-photorealistic Rendering of Volume Models," IEEE Transactions on Visualization and Computer Graphics, vol 7, no 3, July-Sept 2001, pp 253-264.
Homework
  Homework #7 is assigned
  Milestone #3 is due April 13th!

## Slide 119: CSE 591 Volume Visualization II
Ross Maciejewski
rmacieje@asu.edu

## Slide 150: Structuring Feature Space
Ross Maciejewski, Insoo Woo, Wei Chen, David S. Ebert

## Slide 151: Transfer Function Design Is Hard!
Goal is to fit some sort of mathematical transformation to the data that will most faithfully recover essential features within this space
Current widgets rely on inherent data knowledge or trial-and-error

## Slide 152: Transfer Function Design Is Hard!
Density vs. Density Gradient Normal Histogram Feature Space
Application of Transfer Function to Volumetric Data

## Slide 153: Structuring Feature Space
Can we aid users in fitting appropriate mathematical functions to the feature space?
What is a plausible probability density function which describes the dataset?
Our approach is to use kernel density estimation.

## Slide 154: Kernel Density Estimation
Epanechnikov Kernel
N = sample size
= distance from ith
point to kth nearest
neighbor

## Slide 155: Enhancing Transfer Function Design
Density vs. Density Gradient Normal Histogram Feature Space
Color Transfer Function Via Density Estimation Grouping
Application of Transfer Function to Volumetric Data

## Slide 156: Benefits of Structuring Feature Space
Allows users to gain an overview of which areas in the feature space map to volume features

## Slide 157
Density Vs. Density Gradient
Generated Transfer Function
Initial Volume Rendering
Region Exploration Through Transfer Function Interaction
Final Rendering and Transfer Function After Combining and Filtering Regions

## Slide 158: Benefits of Structuring Feature Space
Allows users to gain an overview of which areas in the feature space map to volume features
Allows for easier complex transfer function mapping

## Slide 159: Benefits of Structuring Feature Space
Allows users to gain an overview of which areas in the feature space map to volume features
Allows for easier complex transfer function mapping

## Slide 160: Benefits of Structuring Feature Space
Allows users to gain an overview of which areas in the feature space map to volume features
Allows for easier complex transfer function mapping

## Slide 161: Exploring Feature Space

## Slide 162: Changing Feature Space Axes
Electron orbitals of a two million atom Indium-Arsenic quantum dot device in the second state: (Left) the p orbital rendered using the p-value vs. p-value gradient feature space, (Right) using the p-value vs. s-value feature space.

## Slide 163: Interactive Demo

## Slide 164: Three Dimensional Transfer Function

## Slide 165: Temporally Coherent Transfer Functions
165
1)
11)
21)
31)
41)

## Slide 167: Temporally Coherent Transfer Functions
4380)
4500)
4620)
4740)

## Slide 168: Static Vs. Dynamic Transfer Function
4380)
4500)
4620)

## Slide 169: Future Work Directions
Appropriate distance metrics between features
How to improve understanding of n-dimensional transfer function
Can we “tag” voxels in temporal volumes to track features, or is that necessary?
Region growing may not be the interactions user wants
Can we associate some confidence, uncertainty and/or importance measure to a given cluster
Best distribution method (quantile measures?)

## Slide 170: Questions?

## Slide 171: Readings and Homework
Required Reading:
  Ross Maciejewski, Wei Chen, Insoo Woo, David S. Ebert. Structuring Feature Space - A Non-Parametric Method for Volumetric Transfer Function Generation. IEEE Transactions on Visualization and Computer Graphics, 15(6): 1473-1480, Nov./Dec. 2009.